## Slide 1
LeRobot × SO-ARM101
From Low Loss
to Generalization
A complete engineering loop of a robotic-arm behavior-cloning experiment — and its key finding
Project overview | Data collection · Cloud training · Local deployment · Reflection
2026.05–06
Behavior-cloning baseline
RGB
vision
49 demos
50k steps
ACT
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. [/Sources]

## Slide 2
PROJECT THESIS
Low loss is not the goal — generalization is
02 / 10
We built an end-to-end imitation-learning pipeline, then held “training convergence” up against real deployment.
6.793 → 0.110
training loss, a 98.4% reduction
49
cleaned demonstration episodes
51.7M
ACT policy parameters
No generalization
at deployment
the arm kept reaching toward the most frequent grasp position in training
Core conclusion: a low training loss proves the fit succeeded — by itself it does not prove the vision-to-action policy generalizes.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. [/Sources]

## Slide 3
SYSTEM LOOP
From human demonstration to robot action, end to end
03 / 10
01
Teleoperated collection
Leader → Follower
RGB video + joint states
02
Data governance
anomalous-episode cleanup
v2.1 → v3.0 conversion
03
Cloud training
AutoDL RTX 4090
ACT / 50,000 steps
04
Local deployment
RTX 3060 Ti
camera + Follower execution
The engineering work went far beyond the training script: 18 problems spanning hardware, versions, data formats, and offline environments were each diagnosed and solved.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. [/Sources]

## Slide 4
DATASET
The data let the model converge — and set its limits
04 / 10
Usable training data
49
valid demonstrations (50 planned; 1 anomalous episode removed)
12,625
frames after v3.0 conversion
Observations & actions
Input
front-view RGB 640×480 · 30 FPS
6-DoF arm joint state
Output
6-DoF actions
100-step action chunks
Key limitation
One object type · limited position & container variation · no language annotations.
These gaps mapped directly into the generalization failure.
Note: the raw ZIP preserves the pre-cleanup count of 50 episodes / 12,883 frames; experimental conclusions use the cleaned, converted set of 49 / 12,625.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. The episode/frame-count discrepancy is stated explicitly to avoid reading archival metadata as final experimental data. [/Sources]

## Slide 5
MODEL & TRAINING
ACT encodes vision and arm state into action chunks
05 / 10
Vision encoding
ResNet-18
ImageNet-pretrained
01
Temporal decision
Transformer
4-layer encoder / 1-layer decoder
02
Action generation
VAE + 100-step
action chunks
03
Training setup
AdamW · lr 1e-5 · batch size 8 · dropout 0.1 · 50,000 steps · ~78 minutes
Capacity: 51,668,614 parameters (~207 MB FP32); ~6 GB of VRAM in practice — trained on a cloud RTX 4090, inferred on a local RTX 3060 Ti.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. [/Sources]

## Slide 6
TRAINING EVIDENCE
Smooth convergence — but not the finish line
06 / 10
Chart: training steps
| 0 | 3k | 10k | 20k | 40k | 50k
Training loss | 6.793 | 0.902 | 0.35 | 0.18 | 0.12 | 0.11
98.4%
loss reduction
Deployment is mandatory
Only a real deployment can tell whether the model learned the rule — or a shortcut.
Training logs confirm 50,000 / 50,000 steps completed; the trailing network error came from the automatic push_to_hub upload failing and did not affect the checkpoint.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. [/Sources]

## Slide 7
REAL-WORLD DEPLOYMENT
Confident actions, memorized answers
07 / 10
During training
Overhead Orbbec Astra Pro Plus
Limited position variation
Expert trajectories stay near “correct” states
training distribution: fairly narrow
During inference
Side-view webcam
Object positions changed
Action errors enter unseen states
test distribution: shifted
Observed behavior
Wherever the object was placed, the arm reached toward the most frequent grasp position from training — and kept repeating it.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. Deployment observations come from the engineering journal; the distribution-shift / compounding-error explanation comes from the local reflection notes. [/Sources]

## Slide 8
KEY FINDING
Overfitting can disguise itself as confident action
08 / 10
The textbook picture
low training loss,
worse test metrics
the model memorized samples and fails to generalize
What this project showed
extremely low training loss,
yet a “fixed grasp” in the real scene
it chose the cheapest prediction on the training set — not an understanding of the scene in front of it
Why it matters
This turns “low loss ≠ a reliable policy” from a theoretical claim into reproducible evidence from a real robot deployment.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. [/Sources]

## Slide 9
ROOT-CAUSE ANALYSIS
A joint mismatch across data, model, and deployment
09 / 10
Insufficient data diversity
one object type, unsystematic position variation
Model–data scale mismatch
51.7M parameters facing ~12.6k frames
Missing task intent
pure vision → action, no language conditioning
Train / inference vision mismatch
overhead Astra vs. side-view webcam
Reflection: errors compound in sequential decision-making — one small deviation can carry the arm into states the expert demonstrations never covered.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. Contributions and the distribution-shift account come from the local engineering notes and reflection record; the reflection also proposes augmentation and DAgger-style expert labeling as correctives. [/Sources]

## Slide 10
NEXT STEPS
Turning this failure into the VLA experimental design
10 / 10
01 · A robust baseline first
phase 1
≥ 5 objects × 6 initial positions
Same camera for training and inference
Test whether diversity alone fixes generalization
02 · Close the loop on data
phase 2
Perturbations and augmentation
Let the policy run, collect off-track states
Add expert corrections, DAgger-style
03 · Bring in task intent
phase 3
A language instruction bound to every episode
ACT + CLIP text encoder, or fine-tune a VLA
“Which one to grasp” no longer depends on position
The end goal is not a smaller loss — it is an arm that still completes the task when facing new objects, new positions, and natural-language instructions.
Notes: [Sources] Source: this project's engineering journal, training configs, and reflection notes. The roadmap comes from the project journal and reflection notes; the VLA direction is a next-stage plan, not a result achieved in this stage. [/Sources]